# Audio-Pis

The Audio-Pis are Raspberry-Pis with a Soundcard on top, accompanied with a Set of often used Audio-Adapters. They are used to stream Music from Lounges/Discos/Clubs via Wifi or Ethernet.They are using the Audio Injector Soundcard by FlatmaxStudios.
## Checklist
Audio-PI Checklist
## Parts-List
- Alu-Heatsink for RPi3
- SanDisk Ultra microSDHC 16GB
- Official Raspberry-Pi Plugpack
- Raspberry Pi 3
- Mesh-Bag
- RPi Soundcard "Audio Injector" by FlatmaxStudios
- 3m Stereo Cinch male --> Cinch male Cable
- 6.3cm Mono Klinke male --> Cinch female Adapter - 2x
- 6.3cm Mono Klinke male --> 2x Cinch female Y-Adapter
- 6.3cm Stereo Klinke male --> 2x Cinch female Y-Adapter
- 3.5cm Stereo-Miniklinke male --> 2x Cinch female Y-Adapter
## 3D Printed Cases

We are in the Process of designing and printing Cases for the Audio-Pis including the Soundcards. Here is a Rendering of the Beta, we'll tweet when the Case-Design is finished and tested and it will be publish here.
## Software
The Configuration of the Audio-Pis is managed from our Config-Management, but basicly it runs an ffmpeg-Command reading from alsa, encoding as Opus and pushing to our Icecast-Server. A second transcoding-ffmpeg, running on some server, is then generating the secondary mp3-stream from the primary opus stream.
## AV Meter
They got a visual audio volume meter mounted which can be switched on/off and switch between input and loopback output sound.
https://c3voc.de/wiki/hardware:audio-pis:av-meter