# Video capture and encoding on the Raspberry pi
This page is currently a research collection and commands might not work
## gstreamer pipe gen srt mit kaputtem alsasrc-audio vom usb:
gst-launch-1.0 rpicamsrc inline-headers=true annotation-mode=date+time+frame-number+black-background brightness=60 preview=1 awb-mode=1 bitrate=10000000 exposure-mode=fixedfps sensor-mode=1 keyframe-interval=25 ! 'video/x-h264, width=1920, height=1080, framerate=25/1, profile=high' ! muxout. alsasrc device=hw:1,0 actual-latency-time=12000 buffer-time=200000 ! audioconvert ! avenc_aac ! aacparse ! muxout. mpegtsmux name=muxout ! queue ! srtserversink uri='srt://:8888/'
## funktionierendes audio mit ffmpeg und ner pipe in das srt-tool "srt-live-transmit":
ffmpeg -analyzeduration 500000 -probesize 100000 -threadqueuesize 512 -f v4l2 -inputformat h264 -videosize 1920×1080 -framerate 30 -i /dev/video0 -threadqueuesize 512 -f alsa -sample_rate 44100 -ac 2 -i hw:1 -map 0:0 -map 1:0 -bufsize 0 -af 'adelay=520|520,volume=0dB' -vcodec copy -acodec aac -f mpegts - | srt-live-transmit -v file:con 'srt://:8888&delay=80' -c 1316
ggf vorher im v4l2 codec parameter setzen:
v4l2-ctl -c videobitrate=4000000v4l2-ctl -c h264iframeperiod=25
## rtmp stream from pi cam
raspivid -fps 25 -h 1080 -w 1920 -n -t 0 -g 5 -b 5000000 -stm -o - | gst-launch-1.0 -v fdsrc ! h264parse ! flvmux ! rtmpsink location='rtmp://changeme/stream/bla live=1'
## RTP stream sink and source
raspivid -fps 25 -h 1080 -w 1920 -n -t 0 -b 5000000 -o - | gst-launch-1.0 -v fdsrc ! h264parse ! rtph264pay config-interval=1 ! gdppay ! tcpserversink host=10.23.42.145 port=5000
gst-launch-1.0 -v tcpclientsrc host=10.23.42.145 port=5000 ! gdpdepay ! rtph264depay ! decodebin ! autovideosink sync=false