# Hardware status
This page lists the temporary and constant differences between all cases. When something broke and can not be repaired either order it directly or add it the Shopping page – neitherless add it here, so we have a global overview.
## Lecture room cases (first generation: Case 1 – 4)
New capture cards since 2017-11 geekend:
- 1x Blackmagic Design Decklink Duo 2
  - 4x SDI in/out – currently only two usable
- 2x Blackmagic Design Decklink Mini Recorder
  - 1x SDI in xor HDMI in
### Case 1
additional
- Tally-Set with Raspberry Pi, USB headset and power supply now centralised…
- SD: 1x 128GB, 2x 64 GB, 2x 32GB
missing/broken
- Minion was replaced with 2nd generation minion
- IP Phone (Snom) was replaced with another model
- Klinke-Klinke Kabel in Raumfarbe
- 2x Adapter Cinch auf Klinke (für obiges Kabel)
- Ethernet-Kabel blau (0.3m) irrelevant
- Ethernet-Kabel orange (1,5m) → take spare cable from “Regie 1”-Auerbox
- Audio (XLR) Kappe für Kamera will not be replaced
### Case 2
notes:
- XLR cables from different vendor
- SD Cards: TODO
additional:
1x HDMI Splitter 1×2
### Case 3
notes
- kein HDMI-Splitter 1×2
- SD-Karten: 1x 128GB, 1x 64GB, 2x 32GB
missing
- 2x 3,5mm-Stereo-Klinke → Stereo-Cinch + 4x Cinch→ Mono-Klinke Adapter
- DVI → HDMI Kabel
- HMDI Genderchanger
- Klebeband
additional
…
### Case 4
missing:
second Mini-DP → DVI adapter DVI is sunset, temporary replaced: Mini-DP → Multiport (HDMI, DVI, …) Adapter
## Lecture room cases (second generation: Case 5 – 6)
The second generation does not have following parts by design:
DI-Box passiv ART Direct
New capture cards since 2017-11 geekend:
- 1x Blackmagic Design Decklink Duo
  - 2x SDI in/out
- 2x Blackmagic Design Decklink Mini Recorder
  - 1x SDI in xor HDMI in
### Case 5
missing:
- USB3 SD card reader
- 1x HDMI-Kabel 5m aufgefüllt 2017-11-22
- 1x Ethernet 20m aufgefüllt 2017-11-22
### Case 6
additional:
1x USB 3.0 HDD 2,5“ 2TB in orange mesh bag
missing
- DI Box Behringer DI-20 (aktiv) Acquired but in case 5 for transport to 34c3
- 1x Klinke-Klinke in Raumfarbe
unconfigured and therefore currently not really usable:
Wifi Router TP Link Archer C7 v2
## Regie Box
- 1x USB 3.0 HDD 2,5“ 2TB in orange mesh bag
  - one additional hard drive in lecture room case 6
## Audio cases
### Audio Case 4
Missing:
Micro USB Kabel, zwischen Tablet und Netzteil)== Misc
Tags: Fehlbestand Fehlbestandsliste Kaufen